## Slide 1
KIRD-KIGAM 전문기술교육 – 지하 레이다 탐사
GPR 탐사 실습, 자료처리 및 해석 기술
www.kigam.re.kr
광물자원연구본부
자원탐사개발연구센터
강 웅

## Slide 2
3. GPR Signal Processing
Korea Institute of Geosciences
and Mineral Resources
GPR signal processing techniques
  2D processing
    DC removal
    Dewow
    Correction of zero time
    Time-varying gain
    Background removal
    Filtering in frequency domain
    Filtering in wavenumber domain
    - filtering
    Normal moveout (NMO) correction
    Deconvolution
    Migration
    Velocity estimation
  3D imaging
    Hilbert transform
    3D interpolation
    Slice visualization
    3D volume visualization

## Slide 3
3. GPR Signal Processing
Korea Institute of Geosciences
and Mineral Resources
DC removal & Dewow
  DC removal: 시스템 회로에서 남아있을 수 있는 DC 바이어스 성분의 제거
  Dewow filtering:
    Wow noise 신호의 발생요인
      Induction range의 저주파 성분은 Propagation이 일어나지 않고 지하매질 표면부 및 천부에 확산(Diffusion)되면서, 전기적인 Loop가 형성될 수 있는 주변환경에서 Eddy current에 의한 신호를 Receiver가 받아들일 수 있음 (매우 천천히 Decay되는 파형)
      큰 크기를 가지는 Direct wave 신호에 의해 시스템이 Saturation 되었을 경우 Wow noise를 유발할 수 있음
0
0

## Slide 4
3. GPR Signal Processing
Korea Institute of Geosciences
and Mineral Resources
Correction of zero time
  TX 안테나에서 전자파 펄스의 복사가 이루어지는 시간지점을 기준점으로 함
From Gang Seok Jang, 2006

## Slide 5
3. GPR Signal Processing
Korea Institute of Geosciences
and Mineral Resources
Time-varying gain
  AGC (Automatic Gain Control):
  Multiplies AGC function, which is
  inversely related to reflector
  strength of the raw trace
  SEC (Spreading & Exponential Compensation):
  A composite of a linear time and
  exponential time gain
  Custom gain
Custom gain
Automatic gain control
Spreading & exponential
compensation

## Slide 6
3. GPR Signal Processing
Korea Institute of Geosciences
and Mineral Resources
Background removal
  Air-ground 경계에서 발생하는 클러터를 제거하기 위해 GPR 반사영상에서 평균 (Mean) 혹은 중간값 (Median)을 빼주는 기법을 사용함
    Subtraction of average across all traces
    Subtraction of median across all traces
    Subtraction of moving average
    Subtraction of moving median
  기복이 심한 지형에서 얻어진 GPR 반사영상에서는 Background removal 의 결과가 좋지 않을 수 있음
From G.T. Tesfamariam & D. Mali, 2014

## Slide 7
3. GPR Signal Processing
Korea Institute of Geosciences
and Mineral Resources
Example – Survey line

## Slide 8
3. GPR Signal Processing
Korea Institute of Geosciences
and Mineral Resources
Example – Survey line
Correction of
zero time
Custom
gain
Background
removal